## Slide 1
QUALCOMM TRACK · AI INFRA SUMMIT HACKATHON 2026
PEMA
Personal Environmental Memory Agent
A private, on-device memory of your room for people with low vision or memory loss. Arduino UNO Q (Qualcomm Dragonwing) + Snapdragon Hexagon NPU via GenieX + STM32.
Done by Roshni
PEMA · Qualcomm track · AI Infra Summit Hackathon 2026 · Roshni
1

## Slide 2
What it is: one loop, not a feature list
For 2 billion people with vision impairment, 55 M with dementia
1 Identify locally: name + passphrase on the board. No face data.
2 Remember: YOLOX on the Arduino's Qualcomm chip; where each object was, its usual spot.
3 Notice change: leave and return → "your keys moved from your left to your right."
4 Act: a planner on the Hexagon NPU picks tools: memory, vision, hardware, speech.
5 Verify: every action is read back from the STM32 before it is claimed.
PEMA · Qualcomm track · AI Infra Summit Hackathon 2026 · Roshni
2

## Slide 3
The pipeline
Camera (laptop / phone)
480 px JPEG every ~1.5 s
browser, local network only
Arduino UNO Q · Qualcomm Dragonwing
YOLOX-nano int8, 80 classes
object memory + usual spots
presence + change detection
safety rules + whitelist
SQLite history, dashboard
Snapdragon X Elite · Hexagon NPU · GenieX
Qwen3.5-2B Q4_0, text + vision
planner: 1 tool per step, GBNF grammar
vision: scene questions, room fixtures
profile per call: device, tok/s, TTFT
Arduino STM32U585
sensors every second
matrix · buzzer · relay · servo
get_state readback = verified
local over-temp interlock
Agents, each step visible in the trace: safety → planner → memory / vision / hardware → speech
Board ↔ laptop over USB. Nothing leaves the local network. Same code runs with the model on a Dragonwing board with its own NPU (one URL).
PEMA · Qualcomm track · AI Infra Summit Hackathon 2026 · Roshni
3

## Slide 4
Checking the NPU: measured, not assumed
Per-request proof (GenieX profile)
device = HTP0 (Hexagon), backend = llama.cpp, on every planner step
tokens/s, first token, prompt tokens shown live on the dashboard
Task Manager NPU graph spikes during each answer
Benchmark, same 0.8B Q4_0 model
NPU prefill 297 tok/s · TTFT 0.13 s · decode 17.7
GPU prefill 316 tok/s · TTFT 0.12 s · decode 51.5
CPU prefill 24 tok/s · TTFT 1.60 s · decode 65.9
Agent steps are prompt-heavy: the NPU wins where it matters
Inference optimisation
Q4_0 on the NPU · grammar-constrained decoding (valid JSON every time, 60-120 output tokens) · one multimodal model for planning and vision
compact snapshot prompt, capped memory, 4-step loop with repeat detection · 480 px frames, one in flight
Qualcomm's pre-compiled Qwen3-4B bundle measured at 1077 tok/s prefill, 0.63 s TTFT. Not shipped: QAIRT has no grammar support yet; a hardware-controlling agent needs guaranteed-valid tool calls. One-line switch when it lands.
PEMA · Qualcomm track · AI Infra Summit Hackathon 2026 · Roshni
4

## Slide 5
It notices your keys moved while you were gone, tells you, turns the light on, and proves it did.
Private. On-device. On Qualcomm silicon.
Privacy by design: frames discarded on-device, objects not faces, passphrase not biometrics, camera off switch, no cloud.
Honest limits: the UNO Q's chip has no supported NPU, so the model runs on the laptop's Hexagon; the 3D map is approximate placement from a sweep.
Thank you · Roshni
PEMA · Qualcomm track · AI Infra Summit Hackathon 2026 · Roshni
5